## Slide 1: water desalination plant

## Slide 2
Manufacturing
Sensors and actuators
The presentation is divided into two topics

## Slide 3
In the manufacturing part
Two types
  Membrane desalination
  Thermal desalination

## Slide 4
In the first type(Membrane desalination)
  Reverse Osmosis (RO)
  Structure
  Flow rate
  Electrodialysis (ED) - Membrane-Based Desalination

## Slide 5
In Reverse Osmosis (RO)
Diagram
Principle
Pros and cons
Membrane desalination

## Slide 6: Reverse Osmosis (RO)
Diagram

## Slide 7: Reverse Osmosis (RO)
Utilizes the principle of semipermeable membranes to remove salts and impurities.
Principle

## Slide 8: Reverse Osmosis (RO)
Saline water is pre-treated to remove large particles and impurities.
High pressure is applied to push the water through a semipermeable membrane.
The membrane allows water molecules to pass while blocking salts and other contaminants.
Freshwater (permeate) is collected, and the concentrated brine (reject water) is discharged.
Process

## Slide 9: Reverse Osmosis (RO)
high efficiency
Widely used in desalination of seawater and brackish groundwater
high energy consumption
Sensitive to pollution and the membrane requires periodic maintenance
Pros
Cons

## Slide 10
Membrane desalination
Structure
Intake System
Pre-Treatment System
Desalination Unit
Post-Treatment System
Brine Disposal System

## Slide 11: Structure of intake system
It combines of
  Offshore intake pipes or wells.
  Screens to prevent debris and marine life from entering.
  Pumps to transport water to the pre-treatment system.

## Slide 12: Structure of pre-treatment System
Prepares the raw water by removing large particles, sediments, and microorganisms to protect downstream equipment.
Coagulation and flocculation.
Sedimentation.
Filtration (sand filters or ultrafiltration membranes).
Chemical dosing (e.g., chlorine for disinfection).
Function
Processes

## Slide 13: Structure of desalination Unit
Removes dissolved salts and impurities to produce freshwater.
Membrane-Based.
Thermal-Based.
Function
Types

## Slide 14: Structure of post-treatment System
enhances the freshwater to meet drinking water quality standards.
pH adjustment.
Addition of minerals (e.g., calcium, magnesium) for taste and health.
Final disinfection.
Function
Processes

## Slide 15: Structure of brine disposal System
Handles the discharge of concentrated brine.
Direct discharge into the ocean with proper mixing.
Brine treatment or use in industrial processes.
Function
Methods

## Slide 16: Flow chart

## Slide 17: Flow chart

## Slide 18
Electrodialysis (ED) - Membrane-Based Desalination
Principle
Process
Pros and cons
Membrane desalination

## Slide 19: Electrodialysis (ED) - Membrane-Based Desalination
Uses the principle of ion exchange to separate salts from water.
Saline water passes between alternating cation and anion exchange membranes.
An electric field drives positive and negative ions through their respective membranes, removing them from the water.
The result is desalinated water and a brine stream.
Principle
Process

## Slide 20: Electrodialysis (ED) - Membrane-Based Desalination
Suitable for low-salinity water.
lower power consumption than RO.
Unsuitable for high-salinity water.
Pros
Cons

## Slide 21
In the second type(thermal desalination)
  Multi-Stage Flash (MSF) Distillation
  Multi-Effect Distillation (MED)
  Vapor Compression (VC)

## Slide 22
Multi-Stage Flash (MSF) Distillation
Principle
Process
Pros and cons
Thermal desalination

## Slide 23: Multi-Stage Flash (MSF) Distillation
Relies on the principle of reducing the boiling point of water by lowering the pressure in successive stages.
Principle

## Slide 24: Multi-Stage Flash (MSF) Distillation
Saline water is heated to a high temperature.
In each stage, water is introduced into a low-pressure chamber, causing it to "flash" into steam.
The steam is condensed into freshwater using heat exchangers, while salts remain behind.
The process is repeated across multiple stages for efficiency.
Process

## Slide 25: Multi-Stage Flash (MSF) Distillation
Can handle high salinity water
Widely used in energy-rich countries.
high power consumption.
Pros
Cons

## Slide 26
Multi-Effect Distillation (MED)
Principle
Process
Pros and cons
Thermal desalination

## Slide 27: Multi-Effect Distillation (MED)
Uses the principle of reusing heat energy in successive stages to evaporate and condense water.
Principle

## Slide 28: Multi-Effect Distillation (MED)
Saline water is heated in the first stage to generate steam.
The steam is used to heat water in the next stage, where it evaporates at a lower pressure.
The process repeats over multiple effects to maximize energy efficiency.
Freshwater is condensed and collected at each stage.
Process

## Slide 29: Multi-Effect Distillation (MED)
higher thermal efficiency than MSF.
lower thermal consumption.
requires complex design and operational management.
Pros
Cons

## Slide 30
Vapor Compression (VC)
Principle
Process
Pros and cons
Thermal desalination

## Slide 31: Vapor Compression (VC)
Relies on the principle of compressing and reusing water vapor to reduce energy consumption.
Principle

## Slide 32: Vapor Compression (VC)
Saline water is evaporated, producing steam.
The steam is compressed, raising its temperature and pressure.
The compressed steam condenses to release heat, which is used to evaporate more water.
Freshwater is collected, and the brine is discharged.
Process

## Slide 33: Vapor Compression (VC)
high thermal efficiency.
suitable for small systems.
requires high operational cost for some applications.
Pros
Cons